Included in kit:

- Plastic Pan

- Pan frame

- Chassis

- Axle

- Drawbar

- Wheels

- Hitch

- Foot latch (Not shown)

Tools required:

2 x 17mm wrenches.

2 x 19mm wrenches.

Wheel Brace or

Assembly:

# Text boxes

Attach Wheel to Chassis using the nuts attached to the hubs.  Tighten nuts with a wheel brace,  ensuring that nuts are tight.

Attach drawbar to axle using 2 - M12 x 75mm bolts and nuts.  Attach the drawbar to the chassis using 2 – M12 x 25mm bolts and nuts.

9

6

7

Attach axle to chassis using 4 - M12 x 25mm bolts and nuts ensuring that hinge lugs are facing in opposite direction.

5

4

2

3

1

9)  Nuts,  bolts and spring,  consisting of

M8 x 40mm Carriage bolt - 8 off

M10 x 40mm Hex bolt  - 1 off

M10 x 65mm Hex bolt  - 2 off

M12 x 25mm Hex bolt  - 6 off.

M12 x 40mm Hex bolt  - 2 off.

M12 x 75mm Hex bolt  - 2 off.

M8 Nylock nuts – 8 off

M10 Nylock nuts  - 3 off.

M12 Nylock nuts  - 10 off.

Compression Spring  (23/4” x 13/16” x 0.12”)

Attach hitch to chassis using 2 - M10 x 65mm bolts and nuts.

Attach hitch to chassis using 2 - M10 x 65mm bolts and nuts.

Attach food pedal to the drawbar using M10 x 40mm Hex bolt and nut.  Place compression spring between hitch and plug on the drawbar.  Tighten to remove play in components.

Finished unit

Place pan into pan frame.  Attach using M8 x 40 mm carriage bolts and nuts.